## Slide 1: ERTMS Specifications inside CCS TSI 2023/1695
ERTMS Conference 2024 | Valenciennes
W. Malfait & J. Hernandez Fernandez
Photo: Adobe Srock / by Tobias Arhelger

## Slide 2: Agenda
  Topic 1: ERTMS Specifications inside CCS TSI 2023/1695
  Topic 2: Transition framework inside CCS TSI 2023/1695

## Slide 3: ERTMS Specifications – Digital and Green Rail
Mandate/scope for specifications in CCS TSI 2023/1695 | Link with strategic objectives | Status
Automated Train Operation GoA 1 and 2 | ATO provides capacity benefits and reduces energy consumption (green rail). | 
ETCS Readiness for FRMCS 5G based communication | GSM-R (2G) will become obsolete between 2035-2040 and shall be replaced by FRMCS (5G). Further digitalisation of rail as 5G opens many possibilities. | 
Digital ETCS reducing trackside assets | Hybrid Train Detection: Train integrity allows capacity increase and/or reduced trackside train detection systems. Supervised manoeuvre: Supervised manoeuvre allows safety increase and when using digital automatic coupling will allow to get rid of shunting signals | 
On-board modularity | On-board modularity enables further market opening which allows integration of different interoperability constituents/subsystems from different suppliers (open market). ERTMS specifications include additional specifications which provide on-board modularity focusing on a common Ethernet based system and providing harmonised interfaces between ATO, ETCS, FRMCS parts and RST-subsystem. | 
Additional changes to further optimise capacity, safety & security, cost reductions | The ERTMS specifications are further optimised with additional change requests based on return of experience of ERTMS projects. | 
Notes: Key message: ETCS & ATO Specifications are fully mature and delivered according to the mandate/scope.
Workshop: N/A

## Slide 4: ERTMS Specifications – Evolution of ETCS Baselines/ETCS System versions
CCS TSI 2023/1695 with ETCS Baseline 4 (Release 1)
ETCS B4 R1
(=B4R1 functions up to 2.2 + all other
functional enhancements incl. ETCS
readiness for FRMCS/DAC)
ETCS B4 R1
(= B3R2 functions + all error corrections
+ relocation without linking CR 1370)
SS-153 indicates which on-board
requirements/documents do not
apply or are modified compared to
ETCS up to system version 3.0
SS-153 indicates which on
requirements/documents do not
apply or are modified compared to
B4R1 (ETCS up to system version 3.0)
ETCS B4 R1
(envelope of ETCS system
versions up to 2.2)
(= B4 R1 functions up to 2.1 + ATO)
ETCS B3 MR1
(envelope of ETCS system
versions up to 2.0)
(= B2 functions + error corrections and
functional enhancements incl.
harmonised braking curves and limited supervision)
ETCS B3 R2
(envelope of ETCS system
versions up to 2.1)
(= B3MR1 functions up to 2.0 + error
corrections and functional enhancements incl.
online key management and GPRS/PS)
ETCS B2
(envelope of ETCS system
versions up to 1.0)
CCS TSI 2016/919
set #1 set # 2 set #3
(envelope of ETCS system
versions up to 3.0)
(envelope of ETCS system
versions up to 2.1)
Notes: Workshop:
Explanation of ETCS OBU implementations received today in VA: B3MR1 (partial fulfilment/deviations) or B3R2 (=B3MR1+error corrections without GPRS/online key management)
ETCS & 3 configurations: CCS TSI focuses on 3 standard configurations. Why? short term: error corrections for existing functions including 1370, otherwise NTR could be created; short term (optional): ATO; mid term: ETCS ready for FRMCS/DAC)
ETCS & SS-153: Show table of content

## Slide 5: Agenda
  Topic 1: ERTMS Specifications inside CCS TSI 2023/1695
  Topic 2: Transition framework inside CCS TSI 2023/1695

## Slide 6: CCS TSI 2023/1695 – Transition regimes for innovations based on National Implementation Plans
  Balancing IM/RU economic interests:
  How to handle innovations for the railway system which have a different business case for the Infrastructure Managers and Railway Undertakings.
  Example: Reduce trackside assets (‘digital rail’) might require new mandatory on-board
  functions to be implemented for existing and new vehicles (e.g. Digital Automatic Coupling,
  Train Integrity, FRMCS and associated changes to interface ETCS with FRMCS).
  CCS TSI 2023/1695:
  - National Implementation Plan: Member State’s obligation to balance different expressed needs between impacted stakeholders (IM and RUs) to decide on ATO implementation, new FRMCS radio system or new ETCS system version;
  - If implementation of new functions occurs, framework of a minimum timeframe (notification period) of at least 5 years shall be provided.
Notes: Workshop:
- Limitations of TSI framework on funding criteria (ERA is not economic regulator).
- New: ATO for compatible changes can now be mandatory in case of notification of ATO, but only for impacted vehicle designs
- Change for incompatible changes: FRMCS/DAC: What could we do? Force MSs to reflect on financial migration strategy + minimum notification period of 5 years.

## Slide 7: CCS TSI 2023/1695 – Transition regimes for error corrections (maintenance process)
  EU Policy objective: Providing fully compliant ERTMS products (without errors/deviations/partial fulfilment) allowing vehicles to operate across the EU (without additional restrictions/modifications if the area of use of a vehicle is extended).
  IMs/RUs depend on their suppliers for
  Integration of error corrections in their products.
   Key Commitment #7 of ERTMS MoU 2016:
  Balancing IM/RU economic interests:
    IMs would like that on-board error corrections are implemented in the vehicles in order that temporary mitigation measures can be removed.
    RUs would like that trackside error corrections are implemented in trackside projects in order to allow the operation of TSI compliant vehicles without any restrictions.
  CCS TSI 2023/1695: Responsibility of (the trackside and on-board) suppliers for implementation of errors corrections in products; If errors are preventing normal service in specific projects, IMs and RUs shall implement those corrections within a maximum timeframe of 3 years.
Notes: Workshop:
Explain why is it regulated (e.g. see VA-authorisations with multiple deviations/restrictions; ESC/RSC tests linked to errors; …)?
Explain steps for error corrections

## Slide 8: Feedback from WS 10c & 11b
Mainly clarifications for the understanding and use of appendix B transition regimes and error correction process:
  Applicability at IC, Subsystem or vehicle.
  Impact of production phase of large series.
  Certificates validity according to CCS TSI 2016 vs 2023.
In general well appreciated.
Challenges:
  Coordination of deployment at National/EU level.
  Stability and changes since these are new concepts.
  Planification of error corrections deployment.
  - Reauthorisation processes may be triggered at large scale, procedures to be adjusted.

## Slide 9: THANK YOU
Moving Europe towards a sustainable and safe railway system without frontiers.
Follow us:
Notes: TSI (Transition, Combined Tr),
Revision of TEN-T Regulation: real opportunity to make Trans-European Transport Network fit for the future, to align the development of the TEN-T network to the European Green Deal objectives and the climate targets of the EU Climate Law. Cutting greenhouse gas emissions from the transport sector by 90%, compared with 1990 levels, by 2050, is key to achieving climate-neutrality by the same date.
New intermediary deadline of 2040 to advance the completion of major parts of the network ahead of the 2050 deadline that applies to the wider, comprehensive network. Core network will also be extended.
New term: 9 European Transport Corridors (ECTs) - integration of Core Network Corridors (CNCs) and Rail Freight Corridors (RFCs).
CT-related infrastructure parameters specified (CT profiles for all types of loading units) and strengthen the concept of network resilience by introducing mandatory interconnections between corridors as well as bypass options, with the aim of improving the reliability of transport services.
More transhipment terminals
High-speed rail network between the main nodes of Europe. The major TEN-T passenger rail lines should allow trains to travel at 160 km/h or faster by 2040.