## Slide 1: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
6-7 December 2022

## Slide 2
Josef Doppelbauer
Fabrice Drogoul
Human Factors Expert
Tim Haesevoets
Safety Culture & HOF Officer
Executive Director
Jan Grippenkoven
Teamleader
Nora Balfe
Human Factors Specialist
Jayne Yeo
Project Officer
Cyriel Martin Communication Officer
Speakers – 6 December 2022

## Slide 3: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
Session 3 How are workload and fatigue managed? Infrastructure managers’ perspective

## Slide 4
Time | Description | Speaker
Session 3 ¦ How are workload and fatigue managed? Infrastructure managers’ perspective | Session 3 ¦ How are workload and fatigue managed? Infrastructure managers’ perspective | Session 3 ¦ How are workload and fatigue managed? Infrastructure managers’ perspective
15.30 - 16.10 | Hourly Risk Index at Infrabel: an experimental tool for estimating fatigue risk in incident analysis at traffic control centres | Tim Haesevoets ¦ Infrabel
16.10 -16.50 | Practical Assessment of workload: Case studies from Irish Rail | Nora Balfe ¦ Irish Rail
16.50 - 17.50 | Panel Discussion | Speakers from sessions 1 to 3
17.50 - 18.00 | Close of the day | 
18.00 - 20.00 | Networking cocktail | 
AGENDA | 6 DECEMBER | 15.30- 20.00

## Slide 5
Josef Doppelbauer
Fabrice Drogoul
Human Factors Expert
Tim Haesevoets
Safety Culture & HOF Officer
Executive Director
Jan Grippenkoven
Teamleader
Nora Balfe
Human Factors Specialist
Jayne Yeo
Project Officer
Cyriel Martin Communication Officer
Speakers – 6 December 2022

## Slide 6: Hourly Risk Index at Infrabel
An experimental tool for estimating fatigue risk in incident analysis at traffic control centers
Tim Haesevoets
06/12/2022
Notes: Good afternoon. Thank you for having me at the HF conference.
My name is Tim. I work at Infrabel, the Belgian Infrastructure Manager. Since I’ve been given a stage, I get the chance to talk about myself first. I started my career in 2011 as a traffic and safety controller and eventually became supervisor at the Traffic Control Center of Antwerp. At present day I’m a Safety Culture and Human Factors Officer. As the title might give away, I want to talk to you about a tool I’m experimenting with but first

## Slide 7
Overview
Introduction
Model
Tool
Future

## Slide 8
Notes: let me tell you a secret. While I worked in the Traffic Control Center of Antwerp, I regularly KLIK
Fell asleep while I was working. I fell asleep during the early shift, the late shift and even the night shift. You could say I coped with some fatigue related issues.
Now, I didn’t live near the TCC. Actually, I had to drive 80 kilometres to work, and 80 kilometres back home every shift. So that’s 160 km’s of sleepy Tim, driving his car on the Belgian highways. Although I never actually fell asleep while driving, I did notice I was swerving on the road quite often. At home, I was irritable most of the time. Especially during a streak of 7 consecutive nightshifts. As I addressed those personal observations with colleagues, or frankly, as I just watched around me at work, I could see I wasn’t the only one with those issues.
Currently I don’t work in shifts anymore. I do have two children, a baby and a four year-old that sometimes keep me up at night. But I don’t fall asleep at work anymore, I don’t have problems driving my car and I’m surely not as irritable as I used to be. Don’t ask my wife, she’ll probably tell you otherwise.

## Slide 9
Introduction
Working schedules
7
Notes: I just said something about a span of 7 consecutive nightshifts. I don’t know whether that’s something that’s recognizable in the companies you work for? In the TCC’s at Infrabel this is the maximum amount of consecutive shifts that’s legally allowed, due to our internal rules and regulations. You don’t have to work these streaks all the time of course. There’s also a minimum amount of days off that have to be respected. Now, Why am I telling you this? Because this is the foundation upon which our service schedules are planned out. There is an entity per TCC that’s tasked with planning of personnel. They work with something called “type-schedules”. Those are the standard schedules that the employees are appointed to. As a former TCC employee, I must say that this brings some peace of mind because you have a general idea of how a planned year looks like. Not everyone gets a schedule like this, but I won’t go any further into that. All the schedules are based on legislative constraints, like for instance the 7-shift rule. There is no biological basis for constructing a working schedule.

## Slide 10
Introduction
Workmodes
Notes: Not every day is the same during those consecutive streaks. I always found, and this is my personal opinion, that you have two workmodes in a TCC: one moment you’re underloaded and five seconds later you’re stressed and can’t keep up with work because of an incident or accident occured. And depending on the shift you’re in, you get confronted with rush-hours, or you’re dealing with procedures to put tracks temporariliy out of service for maintenance work, or you’re involved in other safety procedures. So roughly said: your switch is either on, or stand by. Your fatigue is more obvious when you’re in stand-by mode but has more direct consequences when you’re overloaded. If there are more tasks you have to perform and those tasks are also safety-critical tasks then an error due to fatigue has a more noticeable impact on safety. And that’s where my current job comes into play.

## Slide 11
Introduction
HF investigation
Notes: You see, after an employee of a TCC made a noticeable error, the procedure to investigate Human and Organisational Factors comes into play. The procedure consists of two parts. First, there is a decision-tree which guides the decision whether the employee has to be put Off Duty, or can stay On Duty. Put easy, if you, as an employee, have caused a situation where safety has been impacted, you’re put Off Duty. This is done to protect the railway safety and is according to Belgian legislation. The second part is the HOF-inquiry. This is a standard report that’s been made after a designated member from the staff had a deep interview with the employee. The goal is twofold: on one hand to look deeper into HOF but on the other hand also as a coping mechanism for the employee. The story of the employee is heard and he or she gets to ventilate about the safety incident. So it has a caring-component for the employee as well as an investigative component.

## Slide 12
Introduction
5x5
Dynamic
Personal
Intention
Attention
Fatigue
Stress
Awareness
Dynamic
Situational
Pressure
Complexity
Monotony
Prestation
Surroundings
Interactive
Interactions
Relations
Trust
Support
Involvement
Static
Situational
Communication
Instructions
Design
Tools
Context
HOF : 5*5
Static
Personal
Experience
Personality
Motivation
Suitability
Decision
Notes: The HOF that are being observed in the interview are reported in the 5x5 matrix. That is the HOF-model that Infrabel uses that distinguishes 25 different factors. Fatigue is one of these factors.
What my colleague and I do with these reports is we analyse the factors that are being mentioned and put them in a database. This offers us the opportunity to become aware of trends.

## Slide 13
Introduction
Reported fatigue
17%
Notes: Now I’m quite positive that you’re all eager to find out whether or not fatigue has been reported during the interviews.
What we found out is that fatigue was reported 17% of the times. These results are of course very subjective. Depending on the skills of the interviewer, the way of asking questions could be suggestive to the person answering the questions. There is no objective way of measuring fatigue.

## Slide 14
Introduction
Karolinska Sleepiness Scale
Notes: I’m aware of the existence of the Karolinska Sleepiness Scale. In a former version of the HOF-inquiry we actually applied the scale. Employees were asked to rate their fatigue the way they felt 5 minutes prior to the safety incident, according to the scale. What I would like to point out is that when you’re involved in a safety incident is that you get a boost in adrenaline bloodlevels. This makes your heart beat faster and makes you feel more awake. Asking someone to rate themselves in hindsight is therefore not accurate. Besides, the employees have to remember how they were feeling because the HOF-inquiry doesn’t always take place immediately after an incident. Also, for an employee to report fatigue is when this fatigue has reached a level of noticeable tiredness and this tiredness has to stand out from other moments. What I’m trying to say is that this way of reporting only leads to the acknowledgement of extreme values.

## Slide 15
Model
Paper
Notes: Sometimes all you need is a little bit of luck and coincidence. It’s by coincidence that my path crossed the path of my colleague Bart Roets. And it is pure luck that the topic of fatigue came into the conversation. And even more luck is the fact that Bart collaborated with Simon Folkard for his PhD thesis. What was this thesis about? You all know Simon Folkard because of the Risk Index, which calculated a risk in fatigue per shift. The collaboration between Bart and Simon lead to an upgrade and refinement of the theory and tool. It’s to say, it lead to a model that allows to make a prediction of the risk of fatigue per hour, called the Hourly Risk Index.

## Slide 16
Model
Magic
R = RC x RToD x RHoS
Notes: I’m not an academic and to me mathematics is like waving a magic wand, but I’ll try to explain the mechanics behind the model that Simon build and the tool that Bart constructed.
This is the model behind the HRI. Bear with me for a few minutes. First I’ll explain the formula, next I’ll take a deep dive into the individual components. After the theoretical explanation I’ll show you how I use it in an investigative tool. ;
What you see on the screen is the full model. Risk equals cumulative risk times risk at time of day times risk at hours on service. Makes sense, right? Now for the deep dive…

## Slide 17
Model
Cumulative Risk
17
Notes: The Cumulative risk. So this is a relative representation of the cumulative risk. The Y-axis show the relative risk while the X-axis shows the consecutive shifts. The relative risk at the first day is set to one. We see five early shifts, followed by two consecutive rest days in light gray. The middle series represents five consecutive late shifts, followed by two consecutive rest days. The most right series shows five consecutive night shifts, followed by two consecutive rest days

## Slide 18
Model
Time of Day
18
Notes: Next, we see a relative representation of the time of day. Y-axis again is the relative risk while the X-axis shows the time of day during 48 hours. These are scatter plot observations from 6 studies with a cosine fit. I think this is a very interesting graph because it shows a critical point. The relative risk is highest at midnight. For a safety controller in a TCC, this is the busiest time of the night. Most of the safety procedures revolving around protecting workers in a zone where tracks are being put out of service occur around this hour. If we combine this with the former graph where we saw the cumulative risk growing fastest in night shifts we see the risk of fatigue growing.

## Slide 19
Model
Hours on Shift
19
Notes: Finally we see the relative representation of the hours on shift. The Y-axis again the relative risk while the X-axis shows the hours on shift. Important to notice is that there are no breaks calculated in this graph. And that’s a gap in the model. Workload and breaks are not yet being calculated into the model.
We can see that for eight-hour shifts there is nothing striking to report. But after those eight hours, the risk of fatigue goes up and fast.

## Slide 20
Model
Credits
Roets, B., Folkard, S. (forthcoming), Railway traffic controller fatigue, in The Handbook of Fatigue Management in Transportation: Waking Up to the Challenge. CRC Press, Taylor and Francis Group.
Roets, B., Folkard, S. (2022). Estimating hourly work schedule risk in railway traffic controllers. Safety Science. 151.
Notes: You can find more information in the published paper in safety science and in as a chapter book that’s being published soon.
So far the theory. Are you curious to see how I use it for HF investigation?

## Slide 21
Harmony
database
Risk Index
“engine”
Data
Calculation
Visualization
Analysis “after”
(QlikView)
risk trends,
accident investigation
Tool
Design
Notes: Now this is where the real magic happens.
First, on the left hand side we have the first magical ingredient: the input of the data. That’s to say, the data from the harmony database. That’s the database that contains the working schedules for the employees in the TCC’s. In the current version of the experiment we’re working with three TCC’s. The reason behind this is straightforward: I worked in those three TCC’s so I have a deeper understanding of the harmony codes and the workstations behind the codes.
Then we have the model. The model is written in R-code and performs the needed calculations with on data.
And finally the result. A visualisation of the performed calculations in the qlikview application.

## Slide 22
Tool
Graph for Each Hour
Notes: May I have the honour to present you:
The Hourly risk index graph for each hour.
What you can see here is the representation of the relative risk of fatigue for three consecutive nightshifts for a specific person.
What I deliberately omitted from the tool, until now, is the way the calculation is performed. You see, to have a relative risk, you have to have something to compare the specific schedule you’re investigating to. That’s what the red line titled Average HRI represents. That’s the average of all the schedules that are being fed into the program. So all the data that’s being loaded into the R-calculation is calculated into an average and normalised on the Y-axis into the relative risk of 100.
The next thing that stands out is the gray area, or the bars. Those represent the average HRI per shift. The average HRI for all the data that are loaded into the program, without normalisation to 100.
The black line is the data that’s being looked into. That’s the representation of the relative risk per hour for the specific roster, or better: the specific person.
On top there are two lines, the 5% line and the 1% line.
Now for the hard part, the interpretation of the graph. If I take for instance this point, that’s between the hours of one and two am on the third consecutive nightshift. The HRI is 179. That’s a relative risk of fatigue that’s 79 percents higher than the average relative risk of fatigue, but still lower than the 5% and lower than the 1%. So it’s elevated but not to an extreme.
Does this signify anything? This is actually taken from an investigation I was doing where a safety controller made an error. In the interview I was interested whether or not the safety controller was feeling tired or not. He didn’t feel tired but he clicked on a wrong element on the screen by mistake. I was interested to see what the experimental data would teach me. And this is the result. His relative risk of fatigue was elevated by 79 %.

## Slide 23
Tool
Table view
Notes: The graph for each hour is not the only way the data is represented. There are tables that I can use to look for different aspects of the HRI. I can also visualise data in table form.

## Slide 24
Tool
R-FIPS
Notes: The calculation in R is constantly updated. The code will be published on the internet and available for everyone interested. It will be integrated in the R-FIPS package, developed by Curtin University in Australia. The code, as I failed to mention before, will be open source.

## Slide 25
Tool
Issue 1
Data structure
Daat
erutcurts
ataD
Da ta
Struc ture
Struectur
Notes: I want to emphasize the fact that this is an experiment. That means that this is not a fully operational tool. In fact, the visualisation is iteratively updated, as well is the data. It’s not an straightforward process for Bart to integrate all the data from the Harmony database. In fact, he has to first normalise all the data coming from the database because there are differences in geographical areas. The TCC’s are divided over five different areas. The different areas sometimes use the Hamony dbase differently. The input data for the calculations are not always following the same data structure. So it’s mainly a data issue, not an issue with the model.
And of course: how to exactly interpret the results? There’s a difference between what the model predicts and how the person you’re looking into actually feels. The code doesn’t factor in a biological difference like a chronotype. At this point in the experiment we have no way of knowing when the numbers we see are cause for raising alarms. Wat is dan het verschil? Waarom is het zo moeilijk om de data te implementeren?

## Slide 26
Tool
Issue 2
Notes: And of course: how to exactly interpret the results? There’s a difference between what the model predicts and how the person you’re looking into actually feels. The code doesn’t factor in a biological difference like a chronotype. At this point in the experiment we have no way of knowing when the numbers we see are cause for raising alarms. The HRI evaluates the staff schedule, it doesn’t take into account individual human differences.

## Slide 27
Tool
Issue 3
Notes: Finally, and this is my biggest concern, is that the HRI is compared to the average of all the data that’s being put into the calculation. The data is not compared to an ideal planned working schedule, based on a biological basis in stead of a legislative basis.

## Slide 28
Future
Proactive
Notes: For the future, what would my ideal outcome be?
Presently we’re running behind the facts. That’s to say, the HRI experiment is being used to investigate after something happened. It’s not proactively used. That’s what my ideal outcome would be: the HRI being used to plan shifts. To build a roster.

## Slide 29
Future
Challenge
Notes: I didn’t come here just to show you a tool that I’m experimenting with. I came here with a question, a challenge for you. For all of you.
I actually already hinted to the question during my presentation. In my opinion there’s a question to be asked regarding the way working schedules are composed. They are build within the legislative constraints. They are constructed with the system in mind, not with biology in mind. This is something that bothers me because I feel this is a way of thinking that’s not suited anymore in the 21st century. All of us are concerned with human factors, with a human put in the center and the system being built around the human. But not for working schedules.
I want to ask you to rethink the way working schedules are constructed. Not to think about fatigue mitigation but to address the root of the problem: what is biologically the most optimal way to build a working schedule? What is the the evidence based optimal way of rotating in shifts? Do you rotate forward or backwards? Do you work 8h shifts, 10hr, 12hr? How many rest days do you need?

## Slide 30
Notes: What does it take for Tim not to fall asleep at work, not to fight sleep in the car while driving, not to be irritable while performing shift work?

## Slide 31
Keep it safe
Notes: Thank you for your attention.
Do you automatically receive a HOF investigation report after every safety incident?
Does the model allow to predict safety incidents?
Did you feel more fatigued at midnight, or at 3-4 am during a nightshift?

## Slide 32
Notes: Do you automatically receive a HOF investigation report after every safety incident?
Does the model allow to predict safety incidents?
Did you feel more fatigued at midnight, or at 3-4 am during a nightshift?

## Slide 33: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
Session 3 How are workload and fatigue managed? Infrastructure managers’ perspective

## Slide 34
Josef Doppelbauer
Fabrice Drogoul
Human Factors Expert
Tim Haesevoets
Safety Culture & HOF Officer
Executive Director
Jan Grippenkoven
Teamleader
Nora Balfe
Human Factors Specialist
Jayne Yeo
Project Officer
Cyriel Martin Communication Officer
Speakers – 6 December 2022

## Slide 35: Practical assessment of workload: Case studies from Irish Rail
Nora Balfe
Human Factors Specialist

## Slide 36: Contents
What is mental workload?
Why is it important in rail?
Signaller case study
Train driver case study
Conclusions

## Slide 37: Mental Workload: What and why?
The mental demand placed on an operator and their ability to manage it

## Slide 38: Measures of mental workload
Objective
Subjective
Secondary tasks
Physiological
Measures of task demand
Ratings of perceived demand
Performance at a secondary activity
Heart rate, GSR, eye blinks, etc.

## Slide 39: Practical applications of workload measurement
Impact of new technology on attention and concentration?
What effect does automation have?
How many operators?
What size areas?
Workload variability?
How to manage migration?
Notes:   How many operators are needed to safely and efficiently control an area?
  What size areas are appropriate?
  What tasks should and shouldn’t be automated?
  How to safely manage migration of old control areas to new?
  How will the technology affect attention and concentration?
  What tasks are left for the operator and how do they interact?
  Will the technology create peaks and troughs of workload that need to be managed?

## Slide 40: Some examples of current IÉ projects
NTCC
DART+
ETCS
Notes: NTCC – introducing TMS and a better ARS to signalling operations
  Higher level of automation is ‘expected’ to reduce workload
  The actual implementation and limitations of the automation are difficult to understand at design stage
DART+
  Increasing electrification and service frequency in the greater Dublin area
ETCS
  Has implications mainly for train drivers, but also potentially for signallers and controllers

## Slide 41: Signaller Case Study

## Slide 42: Automation reduces workload
Notes: It does, but
Less so under degraded conditions
Workload increases more sharply under automation, which is harder for people to cope with
And, automation is less flexible so you can’t flex staffing levels in the same way as with more basic technologies

## Slide 43: Automation reduces workload
Notes: It does, but
Less so under degraded conditions
Workload increases more sharply under automation, which is harder for people to cope with
Monitoring automation also introduces workload. This can be difficult to quantify/understand and is strongly related to the quality of the automation
And, automation is less flexible so you can’t flex staffing levels in the same way as with more basic technologies

## Slide 44: Workload assessment for signallers
How many signallers will be needed in the new control centre?
What should the boundaries between workstations be?
How can we measure workload in real time to identify when reallocation is needed?

## Slide 45: Predictive Approaches
Demand estimation
Operational judgement
Time Occupancy
TPAM
ODEC/SAS
Mapping

## Slide 46: Real-time approaches
Yet to be developed
Will be based on real-time metrics, e.g.
  Operator actions per minute
  Number of trains under control
  Number of train movements per hour
  Number of communications per hour
  Etc.
Work ongoing to identify the possibilities
  Model will be validated in simulations before deployment

## Slide 47: Driver Case Study

## Slide 48: Train driver workload assessment
Far less published research on driver workload assessment than signaller
Data tends to be based on self-report measures
Underload is a bigger concern than overload
Underload is not simply a matter of paying attention
The infrastructure design has a big influence on workload
New technologies and more reliable trains are tending to further decrease driver workload

## Slide 49: Approach 1: OTDR analysis
Notes: No correlation between heart rate or GSR data and the number of tasks per minute for the driving task
Heart rate is probably more influenced by driver movement, and GSR by external events. Peak here was due to approaching a location of known LRA risk on a day when LRA risk was high.
There might be something in this – all this data was based on a relatively high workload commuter journey. Would be interesting to compare this with a longer intercity journey with less frequent stops. But in practical terms, this measure isn’t mature yet.

## Slide 50: New approach: Route drivability and attentional demand index
The workload imposed on a driver by a particular route
  Network Rail Ergonomics Team developed a Route Drivability Tool to assess this
UK RIS-0703 and RIS-0713 set out requirements for drivability assessment
  Engineering/risk assessment based
  Quite complex
Notes:   RDT:
  Software based
  Modelled the cognitive processes involved in seeing and reacting to features on the route
  Output a workload graph showing peaks in time pressure/demand and attentional conflicts on routes
  Quite complex, and now defunct because software wasn’t maintained

## Slide 51: Why assess route drivability?
To feed in to re-signalling projects, and assess the impact of the proposed scheme on drivers
To support route knowledge – targeting areas of high workload/complexity
To support investigations – identifying whether the workload of that route section could be a contributing factor to events

## Slide 52: Driver Attentional Load Index (DALI)
An index of route attentional demands for each mile of the network
  Based on the features in the section
Data collected from driver assessors on the features that attract attention
  Also ranked by amount of attention commanded by the feature
  Features: e.g. signals, bridges, speed boards, sports grounds, etc.
Data and weightings are still preliminary

## Slide 53: Preliminary data
Identify peaks and troughs in the journey
Plan to also identify conflicts between route features

## Slide 54: Conclusions
Mental workload is the ability of an operator to meet the demands placed on them
Too much or too little demand creates problems
Practical measures of workload can be developed for most roles based on identifying what generates demands
e.g. train movements and infrastructure controlled by signallers and attentional demands on drivers
These measures can be used to help design systems that optimise human performance
Notes: Questions:
What aspects of mental workload do you think we need more research into?
  Underload, peaks and troughs
Is there a role for physiological measures of mental workload?
  In research, yes definitely but they need to be more mature before they are applied in live operations. There are many practical and ethical constraints currently
How can we predict the impact of a new automation system on workload?
  It’s very difficult, but we have to look realistically at what the automation will and won’t do. We often make the assumption that automation will do everything – that’s how it’s usually sold but in practice there are tasks left to the operator and we need to put in the work early on to understand what those are. Then we can try to make some estimates around how demanding they will be under different scenarios as a starting point.

## Slide 55: Thank you for listening! Dr. Nora Balfe Human Factors Specialist, Irish Rail Nora.Balfe@irishrail.ie
Notes: Questions:
What aspects of mental workload do you think we need more research into?
  Underload, peaks and troughs
Is there a role for physiological measures of mental workload?
  In research, yes definitely but they need to be more mature before they are applied in live operations. There are many practical and ethical constraints currently
How can we predict the impact of a new automation system on workload?
  It’s very difficult, but we have to look realistically at what the automation will and won’t do. We often make the assumption that automation will do everything – that’s how it’s usually sold but in practice there are tasks left to the operator and we need to put in the work early on to understand what those are. Then we can try to make some estimates around how demanding they will be under different scenarios as a starting point.

## Slide 56: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
PANEL DISCUSSION day 1
Notes: Jan
Could you please elaborate more on the out of the loop performance problem and the possible solutions?
Could you please elaborate more on how can an entity better take into account Human and Organisational Factors in task analyses and task design (i.e: function allocation man/automation)?
Tim:
Do you automatically receive a HOF investigation report after every safety incident?
Does the model allow to predict safety incidents?
Did you feel more fatigued at midnight, or at 3-4 am during a nightshift?
Nora
What aspects of mental workload do you think we need more research into?
Is there a role for physiological measures of workload?
How can we predict the impact of a new automation system on workload?

## Slide 57
Josef Doppelbauer
Fabrice Drogoul
Human Factors Expert
Tim Haesevoets
Safety Culture & HOF Officer
Executive Director
Jan Grippenkoven
Teamleader
Nora Balfe
Human Factors Specialist
Jayne Yeo
Project Officer
Cyriel Martin Communication Officer
Speakers – 6 December 2022
Notes: Jan
Could you please elaborate more on the out of the loop performance problem and the possible solutions?
Could you please elaborate more on how can an entity better take into account Human and Organisational Factors in task analyses and task design (i.e: function allocation man/automation)?
Tim:
Do you automatically receive a HOF investigation report after every safety incident?
Does the model allow to predict safety incidents?
Did you feel more fatigued at midnight, or at 3-4 am during a nightshift?
Nora
What aspects of mental workload do you think we need more research into?
Is there a role for physiological measures of workload?
How can we predict the impact of a new automation system on workload?