## Slide 1: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
6-7 December 2022

## Slide 2: Speakers – 7 December 2022
Cyriel Martin
Communication Officer
Ole Kroczek
Vanessa García Lozano
Deputy Head of Unit of Railway Safety Coordination
Clarisse Lagaize-Davoine
Project Officer
Safety Manager
Geoffrey Tresontani
ECM Manager
Mark Young
Inspector

## Slide 3: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
Session 6 - How can workload and fatigue be regulated?

## Slide 4
Time | Description |  | Speaker
Session 6 ¦ How can workload and fatigue be regulated? | Session 6 ¦ How can workload and fatigue be regulated? |  | Session 6 ¦ How can workload and fatigue be regulated?
11.20 - 12.00 | How are workload and fatigue integrated in accident investigation? | Mark Young ¦ RAIB (UK Rail Accident Investigation Branch) | Mark Young ¦ RAIB (UK Rail Accident Investigation Branch)
12.00 - 12.40 | Supervision of HOF by AESF (Spanish National Safety Authority) | Vanessa García Lozano ¦ AESF | Vanessa GarcíaLozano ¦ AESF
12.40 - 13.20 | Panel Discussion | Speakers from sessions 4 to 6 | Speakers from sessions 4 to 6
13.20 - 13.30 | Close of the conference |  | 
13.30 - 14.00 | Light lunch |  | 
AGENDA | 7 DECEMBER | 11.20- 14.00

## Slide 5: Speakers – 7 December 2022
Cyriel Martin
Communication Officer
Ole Kroczek
Vanessa García Lozano
Deputy Head of Unit of Railway Safety Coordination
Clarisse Lagaize-Davoine
Project Officer
Safety Manager
Geoffrey Tresontani
ECM Manager
Mark Young
Inspector

## Slide 6
ERA HOF conference, Valenciennes
Integrating workload and fatigue in accident investigation
Mark Young, Inspector, RAIB
7 December 2022

## Slide 7: Overload, underload…
Notes: Plant a seed that overload and underload are two sides of the same coin…

## Slide 8: Near miss at Ufton level crossing, 4 September 2011
Notes: A lot of workload concerns tend to be about overload, and one demonstration of this is in signalling

## Slide 9: Workload assessment
Measurement
  Task analyses (eg timeline)
    Activity analysis
  Primary task
  Secondary task
  Subjective ratings
    Integrated Workload Scale (IWS)
  Physiological
No quantitative ‘red line’ for overload or underload
Notes: But how do we assess that in an investigation – secondary task and physiological are kind of ruled out, so we have some task analysis and subjective techniques

## Slide 10
Notes: Signaller overload was identified as an issue when a train was signalled past a level crossing in Ufton with the barriers raised and the red road traffic signals not flashing (RAIB report 28/2012). An almost continuous stream of tasks in the run-up to the incident, leaving the signaller little spare capacity to review the situation, was probably a factor in his mistakenly setting the route over the crossing.
Near miss incident at Ufton Automatic Half Barrier Crossing, Berkshire, 4 September 2011
Train passed over crossing at 61 mph with barriers raised
Signaller removed reminder on protecting signal along with others associated with the end of possession – but crossing still on local control
Barrier status not displayed adjacent to reminder control
Signaller overload identified as an issue…

## Slide 11: Near miss at Dock Lane level crossing, 14 June 2016
Notes: 13:25 hrs, car given permission to cross UWC when a train coming.
Signaller gave automatic response – familiar nature of call / mental fatigue
High number of crossing calls at Saxmundham (~14 per hour)
Mental demands of maintaining awareness of trains in long track sections

## Slide 12: Workload assessment – Integrated Workload Scale Source: Pickup et al. (2005)
Notes: Use 1-9 numbering for scoring

## Slide 13: Workload assessment – Activity Analysis See Lowe & Pickup (2008)
Time | Snapshot Activities |  |  |  |  |  |  |  |  | No. of Activities | IWS rating | No. trains on panel
17:00 | pap | pap | tel-in | tel-in | route | panel | panel | face | face | 9 | 4 | 2
17:05 | tel-in | tel-in | lx | lx | other |  |  |  |  | 5 | 0 | 3
17:10 | pap | pap | tel-in | tel-in |  |  |  |  |  | 4 | 6 | 3
17:15 | pap | tel-in | tel-in | route | route | panel | other |  |  | 7 | 5 | 3
17:20 | pap | pap | pap | tel-in | tel-in | tel-in |  |  |  | 6 | 5 | 4
17:25 | pap | pap | pap | tel-in | tel-in | tel-in | route | route | panelx2 | 10 | 5 | 4
17:30 | pap | pap | tel-in | tel-in | tel-in | route | panel | panel |  | 8 | 0 | 3
17:35 | pap | pap | tel-in | route | panel |  |  |  |  | 5 | 6 | 2
17:40 | pap | pap | tel-in |  |  |  |  |  |  | 3 | 5 | 2
17:45 | pap | pap | tel-in | tel-in |  |  |  |  |  | 4 | 4 | 2
17:50 | papx4 | tel-inx4 | routex2 | panelx2 | LXx2 |  |  |  |  | 14 | 6 | 2
17:55 | route | panel | panel | lx | lx | face |  |  |  | 6 | 4 | 2

## Slide 14: Workload assessment – Activity Analysis
Notes: Observations helped us understand the nature of the workload – a lot of information being held ‘in the mind’
It became clear that, rather than being an underload issue, this signaller was facing high workload, which led to them becoming mentally fatigued
So there is an interaction between workload and fatigue

## Slide 15: Uncontrolled freight train run-back, Shap, 17 August 2010
Notes: Uncontrolled freight train run-back between Shap and Tebay, Cumbria, 17 August 2010
At 02:04 hrs, train slowed to a stop near Shap summit and ran back for 2.2 miles, reaching a max speed of 51 mph, until driver braked to a stand at 02:09 hrs
Driver was running on single yellows up the hill; cancelled three vigilance warnings and three AWS warnings for (wrong direction) signals while rolling back
Had the driver not braked when he did, the rear of the train would have travelled over a turnout into Tebay sidings at speed, probably derailing and obstructing the adjacent line
Driver on first night shift after five day turns and a rest day
DB Schenker used the HSE’s fatigue and risk index, which implied the driver should be fit to work, but this model under-predicted probability of fatigue on first night shift
Recommendations about fatigue management and mathematical modelling

## Slide 16: Shap, 17 August 2010
Notes: Fatigue is as much about sleep as it is about rosters…
He had been awake for 18 hours – could not sleep in the day before first night shift
  After about 17 hours awake, performance deteriorates to a similar level to that associated with drink-driving (0.05 BAC)
Progressively earlier start times over last few days probably led to sleep loss

## Slide 17: Shap, 17 August 2010
Notes: Given his previous week’s pattern, he was pretty much at his lowest ebb when the incident occurred
Rec 1: DBS to reduce number of shifts that cause fatigue
Rec 2: ORR should provide guidance on shifts that cause fatigue
Rec 3: ORR to provide information to industry on accuracy of fatigue models

## Slide 18: Overturning of a tram at Sandilands junction, 9 November 2016
Notes: 06:07 hrs, 9 November 2016: tram 2551 derailed and overturned on a curve as it approached Sandilands Junction in Croydon
At the time of the accident it was dark and raining heavily
The tram was travelling at approximately 73 km/h (46 mph) as it entered the curve, which had a maximum permitted speed of 20 km/h (13 mph)
Seven people lost their lives in the accident, 19 were seriously injured and 43 had minor injuries

## Slide 19: Analysis – workload
The driver lost awareness of the driving task during a period of relatively low workload
This section of the tram network presents the longest duration of continuous driving with minimal active control by the driver, and is one of the lowest workload sections
  49 s from accelerating after the previous tram stop to the braking point
It is probable that underload led to the driver losing awareness of the driving task on the day of the accident
Notes: Subjective / observational rideout on the network with rudimentary task analysis
Subjective workload ratings of segments of the network from tram operators

## Slide 20: Analysis – fatigue
Underload can affect performance on its own, or it can trigger a microsleep in the absence of fatigue, or it can interact with fatigue to exacerbate the effects on performance
There is no evidence that the driver’s shift pattern carried an exceptional risk of fatigue
The driver reported that he went to bed between 21:30 and 22:00 hrs on the night before the accident, slept well, and was awoken by his mobile phone’s alarm around 03:30 hrs

## Slide 21: Analysis – fatigue
A technical examination of the driver’s mobile phone showed that a document was manually downloaded at about 23:00 hrs on the night before the accident
It is therefore possible that the driver had less than his reported normal 5.5-6 hrs sleep
This amount of sleep is less than the 7-8 hrs that most people need each night
Notes:   It is not known whether the driver remained awake until 23:00 hrs or woke in the night and checked his mobile phone
  Whilst it is possible that the driver needed less than the average amount of sleep, it is also possible that his sleep pattern resulted in him incurring a sleep debt
  Other indications of a sleep debt were that he occasionally slept in the afternoon, and on rest days would naturally sleep longer
  Consistently sleeping less can build up a sleep debt
  Sleep debt cannot just be paid back with extra sleep – need minimum two full nights’ sleep in a row

## Slide 22: Analysis – fatigue
Low workload and a lack of associated stimulation can increase the likelihood of a fatigued person microsleeping
It is therefore possible that a microsleep was a factor in the driver’s loss of awareness on the morning of the accident
It is less likely that a microsleep would have happened in a situation where the driver had a relatively high workload

## Slide 23: Concluding thoughts – underload again…
Notes: Difficulty in identifying redlines for workload – can only say that people were ‘probably’ over/underloaded or that demand was ‘high’ or ‘low’
Future of railways – automation – more likely to see underload cases (though task-related underload – as at Sandilands – remains relevant)

## Slide 24
ERA HOF conference, Valenciennes
Integrating workload and fatigue in accident investigation
Mark Young, Inspector, RAIB
7 December 2022

## Slide 25: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
Session 6 - How can workload and fatigue be regulated?

## Slide 26: Speakers – 7 December 2022
Cyriel Martin
Communication Officer
Ole Kroczek
Vanessa García Lozano
Deputy Head of Unit of Railway Safety Coordination
Clarisse Lagaize-Davoine
Project Officer
Safety Manager
Geoffrey Tresontani
ECM Manager
Mark Young
Inspector

## Slide 27: Monitoring HOF by AESF
Vanessa Mª García Lozano
07/12/2022

## Slide 28: WHY MONITORING HOF?
      Commission Delegated Regulation(EU) 2018/762 of 8 March 2018 establishing common safety methods on SMS requirements
OCURRENCES
INFORMATION KNOWN OR PROVIDED

## Slide 29: IMPORTANCE OF HOF MONITORING
Accidents by cause in national network in Spain-> mainly human factors and installation failures caused.

## Slide 30: IMPORTANCE OF HOF MONITORING
HUMAN FACTOR: In the last two years there are wide variations between consecutive periods.
Chart: Número de accidentes por millón de tren-km
| 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2 | 2018 | 2019 | 2020 | 2021 | 2022
TRABAJOS EN VÍA O IISS | 0.020128 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01992 | 0 | 0.036707 | 0 | 0.052057 | 0.026334 | 0.073997 | 0 | 0.023373 | 0 | 0.043563
ITINERARIO | 0.20128 | 0.058593 | 0.080743 | 0.080521 | 0.080391 | 0.11778 | 0.040347 | 0.05976 | 0.14586 | 0.14683 | 0.054299 | 0.15617 | 0.18434 | 0.14799 | 0.11729 | 0.070118 | 0.067885 | 0.087126
PRESCRIP. CIRCULACIÓN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.049331 | 0 | 0 | 0 | 0.021781
CIRCULAC. MANIOBRAS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.073997 | 0.023459 | 0 | 0.022628 | 0.065344
FORMACIÓN DEL TREN | 0.020128 | 0.039062 | 0.020186 | 0.02013 | 0.020098 | 0 | 0 | 0 | 0 | 0.036707 | 0 | 0 | 0.026334 | 0 | 0.023459 | 0 | 0 | 0.021781
CONDUCCIÓN | 0.060385 | 0.058593 | 0.060557 | 0.02013 | 0.060294 | 0.01963 | 0.040347 | 0.05976 | 0.083347 | 0.18353 | 0 | 0.078085 | 0.026334 | 0.073997 | 0.070376 | 0.093491 | 0.022628 | 0.021781
SEÑALES | 0.080513 | 0.019531 | 0.020186 | 0 | 0.020098 | 0.039259 | 0.020173 | 0.03984 | 0.10418 | 0.11012 | 0.054299 | 0.078085 | 0.052668 | 0.024666 | 0.11729 | 0.046745 | 0.045257 | 0
MTO. MR E INSTAL. | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.022628 | 0.021781
OTROS | 0.020128 | 0.039062 | 0.060557 | 0 | 0.020098 | 0.058889 | 0.040347 | 0 | 0.041673 | 0 | 0.027149 | 0.052057 | 0.079001 | 0.049331 | 0 | 0.023373 | 0 | 0.065344
Notes: Otros. Los errores o transgresiones no incluidas en las causas restantes, así como los calces de mano mal dispuestos.
Señales. Cualquier error o transgresión relacionada con el Libro Segundo de Señales y el Libro Quinto de Sistemas Auxiliares de detección e Instalaciones de Seguridad del RCF, salvo las que se refieren a la incorrecta realización de Itinerarios.
Conducción. Cualquier error o transgresión reglamentaria en la conducción no incluida en los apartados anteriores.
Arranques o paradas bruscas, exceso de velocidad máxima, accionamiento insuficiente del freno de servicio, etc.
Operaciones de circulación en maniobras. Los errores o transgresiones relacionados con la realización de esta actividad no incluidos en los apartados de Señales, Itinerario y Conducción, tales como la dirección y ejecución de la maniobra, comunicación, prescripciones e inmovilización del material.
Prescripciones de circulación. Cualquier error o transgresión en la coordinación y gestión de la circulación o en las órdenes e informaciones transmitidas al maquinista.
Itinerario. Cualquier error o transgresión relacionada con la realización de los Itinerarios de los trenes y el resto de las Normas Reglamentarias incluidas en el Libro Tercero de Circulación del RCF.
Trabajos en vía o Instalaciones de seguridad. Cualquier error o transgresión relacionada con la realización de estas actividades y la aplicación de la normativa vigente de aplicación.

## Slide 31: Index
AESF’s plan and supervision techniques integrating HOF
Examples of HOF supervisión in AESF
B
A

## Slide 32: AESF’s plan and supervision techniques integrating HOF
Techniques
  Audits
  Inspections
AESF framework for planning
Types
  Yearly Planned
  Unplanned

## Slide 33: AUDITS: characteristics
  Especific or planned.
  Generally based documented and interviews
  Directly addressed to selected staff
  General, based on SMS requirements
AESF’s plan and supervision techniques integrating HOF

## Slide 34: AUDITS: areas and topics for HOF control
  Working shifts. Driving times.
  Soft skills training
  Human factor experts
  Risk management
  Leadership audit
AESF’s plan and supervision techniques integrating HOF

## Slide 35: AESF’s plan and supervision techniques integrating HOF
  On the ground
  With train drivers and/or other railway staff
  Provision of tools for the service. SMS procedures.
  Simple questions designed to assess the integration of the SAFETY culture and the human factor by operational staff.
OPERATIONAL INSPECTIONS: characteristics

## Slide 36: AESF’s plan and supervision techniques integrating HOF
  Do you consider that your training is sufficient to perform your duties safely?
  When you detect a safety risk, do you report it? to whom? what channels do you follow?
  Do you consider that the procedures provided by your company are useful and adapted to the way you perform your duties? What procedures are you familiar with?
  Are you aware of your company's safety policy?
  Do you take care of your rest habits in order to report to work?
OPERATIONAL INSPECTIONS: example of questions

## Slide 37: Index
AESF’ plan and supervision techniques integrating HOF
Examples of HOF supervision in AESF
B
A

## Slide 38
  Driving times and breaks
  Work days
  Rest periods
Examples of HOF supervision in AESF
1. GENERAL INSPECTION: design of working shifts and driving times

## Slide 39: 2. SPECIFIC INSPECTION: after a complaint received
Examples of HOF supervision in AESF
Actions taken by AESF: Investigations and request of information

## Slide 40: 2. SPECIFIC INSPECTION: after a complaint received
  In two days, 7 inspections were carried out.
    2 inspections on line R4
    2 inspections on line R1
    1 inspection at France Station
    2 inspections on line R2norte
Examples of HOF supervision in AESF
Actions taken by AESF: inspection

## Slide 41: 2. SPECIFIC INSPECTION: after a complaint received
?
Examples of HOF supervision in AESF
Actions taken by AESF: Recommendation for the sector

## Slide 42
  NIB RECOMMENDATIONS
    35/2017 – 5 Promote, in collaboration with the different actors in the industry, an analysis of possible complementary devices to the "dead man" that can detect (and respond to) situations of semi-consciousness.
    35/2017 - 4 Include tests or questionnaires aimed at detecting possible risks of sleep disorders in the regular medical tests carried out on drivers, so that preventive measures can be taken in this respect.
2017/07/28 Barcelona Françe Station
Collision with molehill
The direct cause of the accident was the driver's failure to apply the brakes.
Examples of HOF supervision in AESF
3. SPECIFIC SUPERVISION ACTIVITY: arising from events

## Slide 43
NSA-ES launches a consultation on the NSAs Network
Consult with industry to see if fatigue detection devices are being developed.
NSAs to monitor companies on the design of drivers' working hours.
Research on existing options for other means of transport
Examples of HOF supervision in AESF
Actions taken by AESF
3. SPECIFIC SUPERVISION ACTIVITY: arising from events

## Slide 44
Case study and publication of recommendations by the Railway Medicine Committee driven by the NSA ES
Spain starts incorporating more monitoring of sleep pathologies in periodic psychophysical checks.
Actions taken by AESF
Examples of HOF supervision in AESF
3. SPECIFIC SUPERVISION ACTIVITY: arising from events

## Slide 45
Examples of HOF supervision in AESF
4. SPECIFIC ACTIONS: after data analysis
Spad increased tendency observed in 42% in 5 years

## Slide 46
Examples of HOF supervision in AESF
4. SPECIFIC ACTIONS: after data analysis
Spad increased tendency observed in 42% in 5 years
Spad by type of service
Actions taken by AESF:
Compilation of information
Data analysis
Chart: 
| Entrada | Maniobra | Retroceso | Salida | Sin información
Columna2 | 25 | 11 | 3 | 56 | 5
Spad by place

## Slide 47
Examples of HOF supervision in AESF
4. SPECIFIC ACTIONS: after data analysis
Spad increased tendency observed in 42% in 5 years
Actions taken by AESF:
Compilation of information
Data análisis
First conclussions
  Objective causes were identified (lack of visibility, insufficient distance between signals, etc)
  No possibility to identify HOF due to the data requested and provided
  Need for additional information to correctly address the cause-effect relation (organizational factors, drivers behaviour, etc)
  Extend the investigation to include underlying factors

## Slide 48
  Information reported system in AESF on circumstances producing spad.
  Information from all actors involved since the beginning.
  Confidentiality is granted.
  Information based in HF methodology of RSSB or similar.
  General templates for providing information have beendrafted
Examples of HOF supervision in AESF
4. SPECIFIC ACTIONS: after data analysis
Spad increased tendency observed in 42% in 5 years
Actions taken by AESF:
Compilation of information
Data análisis
First conclussions
Reported system in AESF

## Slide 49
Rebase
Empresa Ferroviaria
Administrador de infraestructuras
Personal Circulación
Maquinista
Modelo Ficha
Entrega ficha
a su personal
Entrega ficha
a su personal
Cauce
confidencial
Cauce
confidencial
Obligación
de cubrir
ficha
Obligación
de cubrir
ficha
Examples of HOF supervision in AESF
4. SPECIFIC ACTIONS: after data analysis
Spad increased tendency observed in 42% in 5 years
Actions taken by AESF:
Compilation of information
Data análisis
First conclussions
Reported system in AESF

## Slide 50: Thank you for your attention ¿Questions?
Vanessa mª García Lozano
vmgarcia@seguridadferroviaria.es
Notes: How considers and guarantee AESf the confidentiality of staff that request it?
What are the actions that AESF starts if an unfulfillment is detected in HOF?
Does AESF has an estimation of HOF integration in the Spanish railway sector?

## Slide 51: Conference - Integration of Human and Organisational Factors: Managing Workload and Fatigue
PANEL DISCUSSION day 2

## Slide 52: Speakers – 7 December 2022
Cyriel Martin
Communication Officer
Ole Kroczek
Vanessa García Lozano
Assessor
Clarisse Lagaize-Davoine
Project Officer
Safety Manager
Geoffrey Tresontani
ECM Manager
Mark Young
Inspector